## Slide 1
Makers Conclave 2026
SentinelX – Edge AI Fall Risk Prediction & Prevention Wearable
Problem Statement ID: MC-48 | AI-Powered Fall Prevention Wearable for Elderly
Team : SentinelX | Team Leader’s NIAT ID: N25B01A0097 | Submission:
Campus Name: SVYASA BANGALORE
Team Members
  Sankirth R Bhat — N25B01A0097 — CSE
  Manish P Shetty — N25B01A0148 — CSE
  N Darshit — N25B01A0074 — CSE
  Nitish Kumar — N25B01A0089 — CSE
  Submission Date: 02-03-2026
N25B01A0097 | Problem ID: MC-48
Notes: 1

## Slide 2
Problem Understanding & Solution Approach
The Challenge
Elderly falls cause severe injuries and delayed medical response. Existing solutions detect falls after impact, are costly, or rely on cloud connectivity. We need an affordable system that predicts risk early, detects falls reliably, and alerts caregivers immediately.
Our Solution
A low-cost wearable using MPU6050 motion sensor connected to ESP32 running edge ML model for real-time analysis.
Pre-fall Detection
🧠 Motion Pattern → Instability Score → Risk Flag
Fall Classification
Impact event detection with high accuracy
Context Logic
Location-aware sensitivity adjustment
Alert System
Buzzer + SMS to caregiver
A 0.96” OLED display
Provides real-time status feedback (SAFE / RISK / FALL DETECTED).
≥90%
Detection Accuracy
Target fall-event detection
<200ms
Alert Latency
On ESP32 processing
≤₹2.5K
Device Cost
Total BOM budget
N25B01A0097 | Problem ID: MC-48
Feature | Existing Bands | SentinelX
Pre-Fall Prediction | ❌ | ✅
Offline Processing | ❌ | ✅
Cost < ₹3000 | ❌ | ✅
Scenario: Elder walking → instability spike → model detects RISK →
buzzer vibrates → fall detected → SMS sent in 150ms
Notes: 2

## Slide 3
Inventory & Component Feasibility
Component
Purpose
Status
Cost (₹)
ESP32 DevKit V1
Edge compute + Wi-Fi
To Purchase
500
MPU6050 IMU
Motion sensing
To Purchase
150
SIM800L GSM Module
SMS alert
To Purchase
400
Buzzer + Vibration
On-device alert
To Purchase
120
Li-ion Battery + Charger
Portable power
To Purchase
350
Enclosure + Strap
Safety + usability
To Purchase
300
Wiring + Perfboard
Connections
To Purchase
150
0.96” I2C OLED (128x64)
Real-time visual status display
To Purchase
200
Laptop (existing)
Model training
Already Owned
0
TOTAL
₹2,170
Software Stack & Development Tools
Arduino IDE / PlatformIO
ESP32 firmware development and deployment
TensorFlow Lite Micro
On-device ML inference optimization
Python (NumPy, Pandas)
Data processing and model training
Dataset Source
Self-collected IMU samples + augmentation
N25B01A0097 | Problem ID: MC-48
MPU6050 → ESP32 (Edge ML) →
| | |
OLED Buzzer GSM SMS
Notes: 3

## Slide 4
60-Day Timeline & Milestones
Phase
Duration
Key Tasks
Milestone
Phase 1
Week 1-2
Procure components, sensor calibration, collect IMU samples (normal vs stumble vs fall)
Clean dataset + baseline thresholds
Phase 2
Week 3-4
Train lightweight classifier (Decision Tree / 1D-CNN), evaluate accuracy, reduce false positives
Model ≥85% baseline + confusion matrix
Phase 3
Week 5-7
Convert to TFLite Micro, deploy on ESP32, implement context-aware thresholds, integrate GSM + buzzer + OLED display, implement real-time status UI
Real-time edge inference + alert triggers
Phase 4
Week 8
Field testing with multiple patterns, tune thresholds, finalize enclosure, document results
Working PoC demo + documentation
Risk & Contingency Plan
Risk: False positives during daily activities
Mitigation: Add smoothing window + activity gating (standing/walking detection) + threshold calibration per user
N25B01A0097 | Problem ID: MC-48
Notes: 4

## Slide 5
Impact, Innovation & Execution
🌍 Impact
Affordable, real-time fall risk prediction for elderly individuals living independently. Reduces delayed medical response and improves home safety in Indian households.
🚀 Innovation
  Pre-fall instability detection
  Context-aware sensitivity
  Fully offline Edge AI on ESP32
  Low-cost design (~₹2,000)
  Minimal on-device visual interface for real-time risk transparency
📈 Scalability
Home prototype → Elder-care facility deployment → IoT integration with optional dashboard for caregivers.
Why SentinelX
Team Strengths
  Clear division of tasks: embedded systems, edge ML deployment, testing & evaluation
  Focused, feasible 60-day execution plan
  Hands-on experience with ESP32 and sensor integration
Our Commitment
Delivering a working edge-based fall risk prediction and alert prototype within 60 days, meeting all technical specifications and performance targets.
N25B01A0097 | Problem ID: MC-48
Notes: 5